| GPS TUNER 5.4P You can download WM OS mobile GPS Tuner Geo 5.4p installer from here: http://www.megalith.hu/data/GPSTuner_v54p_installer.exe Desktop for Raster Map Calibrator installer and user manuals: http://gpstuner.com/5.4/download/ Registration website: http://gpstuner.com/5.4/registration |
| --- |
| E | D | C | B | A |
| 1st Tier Trip Computer | 1st Tier Map Icon | 1st Tier Compass | 1st Tier Waypoint Manager | 1st Tier GPS panel |
| 2ND Tier :- Trip computer speedometer | 2ND Tier :- Map Settings (3 pages) | 2ND Tier :- Options & Target | 2ND Tier :- Available options are :- ADD WAYPOINT TRACKLOG NMEA LOG START GPS SHARE | 2ND Tier :- Sub Setting Options are :- GPS UNITS TRACK MAP OTHER |

| A 1st Tier GPS panel | 2ND Tier :- Sub Setting Options are :- GPS settings UNITS settings TRACK settings MAP settings OTHER settings Screen shots of Sub Setting Options under GPS PANEL |
| --- | --- |
| 1.GPS settings | 1. | 2. | The GPS tuner software would auto detect the GPS com port number. For Motorola ES 400 the internal GPS com port is COM 6, the external GPS com port is COM 2. Baud rate is 9600. |  |
| 2. UNITS settings | 1. | The recording of waypoint in GPS Tuner will always be in default WGS84, as per SOI’s latest mapping policy. Users to make Note: - Kindly ignore using India- Bangaldesh datum data into all receivers as the transformation parameters are not uniform and they will not be the same as per SOI’s data. |  |
| TRACK settings | 1. | Selection of Autostart and Autosave will automatically record and save your tracklog once GPS lock is achieved. Setting GPS vertex intervals to the minimum gap-length will help define a more detailed path line traversed. Ex., A curved road would show a smooth turn / curve. |  |
| A 1st Tier GPS panel MAP settings | 1 Various Map type are accessible. Further with GPRS enabled SIM card, Google data can be accessed in GPS Tuner. | 2. For raster images/ bitmaps see explanation under GPS tuner’s desktop software called MAP Calibrator. Here the JPEG raster image with its geo referenced combination file in *.gci format is to be imported into PDA, from desktop. At the PDA the geo-referenced raster image directory path is to be defined, by selecting the yellow icon folder. The relevant geo-referenced scanned map /raster image will appear while changing map locations. |  |
|  | 3. | 4. |  |

| A 1st Tier GPS panel OTHER |  | BY selecting POPUP , information of the past recorded waypoint records will be highlighted while travelling klog |  |  |
| --- | --- | --- | --- | --- |

| B 1st Tier Waypoint Manager 2nd tier option ADD WAYPOINT | 2ND Tier :- Available options are :- ADD WAYPOINT 2. TRACKLOG 3. NMEA LOG 4. START GPS SHARE |
| --- | --- |
|  | select to record /add waypoint Tracklog to be GREEN NMEA select to GREEN if you want playback of the tracklog path animation |  |
|  | Take a picture of the waypoint Use top to write note-text descriptions for the waypoint. is the keyboard icon | Save your waypoint. Waypoint is recorded in default WGS84 only as per contemporary practice. SOI has also made WGS 84 the mandatory mapping datum. |
| B 1st Tier : Waypoint Manager 2nd tier option Contd: ADD WAYPOINT | tool is to locate the waypoint by text or distance To save file of list seen below the user desires. To open the above selections directory location of the past saved files . | Select the desired waypoint for relevant GPS related options. To navigate to the desired waypoint ...”Set as target” Locate on map is to search waypoint on MAP View Modify waypoint is used for editing the waypoint value. |
|  | The GPS Tuner saving formats are :- * .gpx format ( not Garmin format) *.kml ( waypoint with its picture will appear on earth Google) *.sdf |  |
| Important note:- | Saved Data should not be CUT pasted to desktop. Saved Data should be COPY pasted to the desktop from PDA. |
| C 1st Tier Compass 2ND Tier :- Options & Target for Navigating to waypoint. | Following the pointer direction reach destination. Click center of Dial for more details. Unlock LOCK to stop navigation. |  |

| D 1st Tier Map Icon |  | The geo-referenced raster image in the background shows the current GPS in a white circle. The waypoint destination is the target. Red-circled 1 and 2 show the points that were used for ge0referenceingthe raster world. Map Use desktop MAP calibrator software from http://gpstuner.com/5.4/download/ |
| --- | --- | --- |
| 2ND Tier :- Map Settings (3 pages) |  | Area calculation Passive method:- Click blue polygon Select red button Then touch map to start the area to measure polygon’s start point. Next alternate stylus to touch green button with the various polygon vertices. Active mehod:- Click blue button Select red button to start reording the tracklog. Finish track log. Area polygon is completed. |